## Slide 1: P&S Modern SSDs Fine-Grained Mapping & Multi-Plane Operation-Aware Block Management
Dr. Mohammad Sadrosadati
Prof. Onur Mutlu
ETH Zürich
Fall 2022
14 December 2022

## Slide 2: Recap: What We Have Discussed So Far
SSD Organization
NAND Flash Organization and Operations
Advanced NAND Flash Commands
FTL: Address Translation & Garbage Collection

## Slide 3: Today’s Agenda
Fine-Grained Mapping
Multi-plane Operation-Aware Blk. Mgmt.
Fine-Grained Mapping
Multi-plane Operation-Aware Blk. Mgmt.

## Slide 4: I/O Mismatch b/w OS and NAND Flash
The page size (i.e., minimum I/O unit) of NAND flash memory has continuously increased
  From 256 bytes to 16 KiB
  Low area overhead and high bandwidth (size / latency)
The logical block (or sector) size of file systems has also increased
  From 512 bytes to 4 KiB
  To more efficiently work with NAND flash-based SSDs
  Increasing the block size is not straightforward
    I/O handling is closely related to OS memory management
    Memory page size = 4 KiB
    Unnecessary fetch or eviction at the page cache

## Slide 5: Small Write Requests
Inefficiencies due to the erase-before-write property
Req (LBA: 0x04, Size: 1, DIR: W, Data: A)
4-KiB Offset
16-KiB Page Number
LPA | PPA
0x00 | -
0x01 | -
0x02 | -
0x03 | -
0x04 | -
0x05 | -
… | …
0x00 |  |  |  | 
0x01 |  |  |  | 
0x02 |  |  |  | 
0x03 |  |  |  | 
0x04 |  |  |  | 
0x05 |  |  |  | 
0x06 |  |  |  | 
… |  |  |  | 
PPA
Block 0
Block 1
16 KiB
0b 0000 0000 0000 0100

## Slide 6: Small Write Requests
Inefficiencies due to the erase-before-write property
Req (LBA: 0x04, Size: 1, DIR: W, Data: A)
0b 0000 0000 0000 0100
4-KiB Offset
16-KiB Page Number
LPA | PPA
0x00 | -
0x01 | -
0x02 | -
0x03 | -
0x04 | -
0x05 | -
… | …
0x00 | A |  |  | 
0x01 |  |  |  | 
0x02 |  |  |  | 
0x03 |  |  |  | 
0x04 |  |  |  | 
0x05 |  |  |  | 
0x06 |  |  |  | 
… |  |  |  | 
PPA
Block 0
Block 1
16 KiB

## Slide 7: Small Write Requests
Inefficiencies due to the erase-before-write property
Req (LBA: 0x04, Size: 1, DIR: W, Data: A)
0b 0000 0000 0000 0100
4-KiB Offset
16-KiB Page Number
LPA | PPA
0x00 | -
0x01 | 0x00
0x02 | -
0x03 | -
0x04 | -
0x05 | -
… | …
0x00 | A |  |  | 
0x01 |  |  |  | 
0x02 |  |  |  | 
0x03 |  |  |  | 
0x04 |  |  |  | 
0x05 |  |  |  | 
0x06 |  |  |  | 
… |  |  |  | 
PPA
Block 0
Block 1
16 KiB

## Slide 8: Small Write Requests
Inefficiencies due to the erase-before-write property
Req (LBA: 0x01, Size: 2, DIR: W, Data: B, C)
LPA | PPA
0x00 | -
0x01 | 0x00
0x02 | -
0x03 | -
0x04 | -
0x05 | -
… | …
0x00 | A |  |  | 
0x01 |  |  |  | 
0x02 |  |  |  | 
0x03 |  |  |  | 
0x04 |  |  |  | 
0x05 |  |  |  | 
0x06 |  |  |  | 
… |  |  |  | 
PPA
Block 0
Block 1
0b 0000 0000 0000 0001
4-KiB Offset
16-KiB Page Number

## Slide 9: Small Write Requests
Inefficiencies due to the erase-before-write property
Req (LBA: 0x01, Size: 2, DIR: W, Data: B, C)
0b 0000 0000 0000 0001
4-KiB Offset
16-KiB Page Number
LPA | PPA
0x00 | -
0x01 | 0x00
0x02 | -
0x03 | -
0x04 | -
0x05 | -
… | …
0x00 | A |  |  | 
0x01 |  | B | C | 
0x02 |  |  |  | 
0x03 |  |  |  | 
0x04 |  |  |  | 
0x05 |  |  |  | 
0x06 |  |  |  | 
… |  |  |  | 
PPA
Block 0
Block 1

## Slide 10: Small Write Requests
Inefficiencies due to the erase-before-write property
Req (LBA: 0x01, Size: 2, DIR: W, Data: B, C)
0b 0000 0000 0000 0001
4-KiB Offset
16-KiB Page Number
LPA | PPA
0x00 | 0x01
0x01 | 0x00
0x02 | -
0x03 | -
0x04 | -
0x05 | -
… | …
0x00 | A |  |  | 
0x01 |  | B | C | 
0x02 |  |  |  | 
0x03 |  |  |  | 
0x04 |  |  |  | 
0x05 |  |  |  | 
0x06 |  |  |  | 
… |  |  |  | 
PPA
Block 0
Block 1

## Slide 11: Small Write Requests
Inefficiencies due to the erase-before-write property
Req (LBA: 0x01, Size: 2, DIR: W, Data: B, C)
0b 0000 0000 0000 0001
4-KiB Offset
16-KiB Page Number
LPA | PPA
0x00 | 0x01
0x01 | 0x00
0x02 | -
0x03 | -
0x04 | -
0x05 | -
… | …
0x00 | A |  |  | 
0x01 |  | B | C | 
0x02 |  |  |  | 
0x03 |  |  |  | 
0x04 |  |  |  | 
0x05 |  |  |  | 
0x06 |  |  |  | 
… |  |  |  | 
PPA
Block 0
Block 1
Why at the middle of the page?
  To keep the 4-KiB offset: mapping table stores only the index of the 16-KiB page!
Why not using the unused space in physical page 0x00?
  That space is already mapped to logical pages 0x05~0x07 (not written yet).

## Slide 12: Small Write Requests
Inefficiencies due to the erase-before-write property
Req (LBA: 0x07, Size: 1, DIR: W, Data: D)
0b 0000 0000 0000 0111
4-KiB Offset
16-KiB Page Number
LPA | PPA
0x00 | 0x01
0x01 | 0x00
0x02 | -
0x03 | -
0x04 | -
0x05 | -
… | …
0x00 | A |  |  | 
0x01 |  | B | C | 
0x02 |  |  |  | 
0x03 |  |  |  | 
0x04 |  |  |  | 
0x05 |  |  |  | 
0x06 |  |  |  | 
… |  |  |  | 
PPA
Block 0
Block 1
  Q: Can we use the unused space?
  A: Not likely, because
    Data randomization – Cells in the unused space have been already programmed.
    Program-order constraint – Re-programming physical page 0x00 can affect the reliability of the data stored in physical page 0x01.

## Slide 13: Small Write Requests
Inefficiencies due to the erase-before-write property
Req (LBA: 0x07, Size: 1, DIR: W, Data: D)
0b 0000 0000 0000 0111
4-KiB Offset
16-KiB Page Number
LPA | PPA
0x00 | 0x01
0x01 | 0x00
0x02 | -
0x03 | -
0x04 | -
0x05 | -
… | …
0x00 | A |  |  | 
0x01 |  | B | C | 
0x02 |  |  |  | 
0x03 |  |  |  | 
0x04 |  |  |  | 
0x05 |  |  |  | 
0x06 |  |  |  | 
… |  |  |  | 
PPA
Block 0
Block 1
Unused yet discarded
Small writes cause waste of P/E cycles:
More frequent garbage collections  Performance and lifetime degradation

## Slide 14: Small Write Requests
Inefficiencies due to the erase-before-write property
Req (LBA: 0x07, Size: 1, DIR: W, Data: D)
0b 0000 0000 0000 0111
4-KiB Offset
16-KiB Page Number
LPA | PPA
0x00 | 0x01
0x01 | 0x00
0x02 | -
0x03 | -
0x04 | -
0x05 | -
… | …
0x00 | A |  |  | 
0x01 |  | B | C | 
0x02 |  |  |  | 
0x03 |  |  |  | 
0x04 |  |  |  | 
0x05 |  |  |  | 
0x06 |  |  |  | 
… |  |  |  | 
PPA
Block 0
Block 1
A |  |  | 
Read

## Slide 15: Small Write Requests
Inefficiencies due to the erase-before-write property
Req (LBA: 0x07, Size: 1, DIR: W, Data: D)
0b 0000 0000 0000 0111
4-KiB Offset
16-KiB Page Number
LPA | PPA
0x00 | 0x01
0x01 | 0x00
0x02 | -
0x03 | -
0x04 | -
0x05 | -
… | …
0x00 | A |  |  | 
0x01 |  | B | C | 
0x02 |  |  |  | 
0x03 |  |  |  | 
0x04 |  |  |  | 
0x05 |  |  |  | 
0x06 |  |  |  | 
… |  |  |  | 
PPA
Block 0
Block 1
A |  |  | D
Read
Modify

## Slide 16: Small Write Requests
Inefficiencies due to the erase-before-write property
Req (LBA: 0x07, Size: 1, DIR: W, Data: D)
0b 0000 0000 0000 0111
4-KiB Offset
16-KiB Page Number
LPA | PPA
0x00 | 0x01
0x01 | 0x00
0x02 | -
0x03 | -
0x04 | -
0x05 | -
… | …
0x00 | A |  |  | 
0x01 |  | B | C | 
0x02 | A |  |  | D
0x03 |  |  |  | 
0x04 |  |  |  | 
0x05 |  |  |  | 
0x06 |  |  |  | 
… |  |  |  | 
PPA
Block 0
Block 1
A |  |  | D
Read
Modify
Write

## Slide 17: Small Write Requests
Inefficiencies due to the erase-before-write property
Req (LBA: 0x07, Size: 1, DIR: W, Data: D)
0b 0000 0000 0000 0111
4-KiB Offset
16-KiB Page Number
LPA | PPA
0x00 | 0x01
0x01 | 0x02
0x02 | -
0x03 | -
0x04 | -
0x05 | -
… | …
0x00 | A |  |  | 
0x01 |  | B | C | 
0x02 | A |  |  | D
0x03 |  |  |  | 
0x04 |  |  |  | 
0x05 |  |  |  | 
0x06 |  |  |  | 
… |  |  |  | 
PPA
Block 0
Block 1
A |  |  | D
Read
Modify
Write
Small writes cause read-modify-writes: Waste of P/E cycles + additional read operations  Performance and lifetime degradation

## Slide 18: Fine-Grained Mapping + Page Buffer
Write a page only when there are sufficient data blocks
Req (LBA: 0x04, Size: 1, DIR: W, Data: A)
LPA | PPA
0x00 | -
0x01 | -
… | -
0x04 | -
… | -
0x07 | -
… | …
0x00 | 0x01 | 0x02 | 0x03
0x04 | 0x05 | 0x06 | 0x07
0x08 | 0x09 | 0x0A | 0x0B
0x0C | 0x0D | 0x0E | 0x0F
0x10 | 0x11 | 0x12 | 0x13
0x14 | 0x15 | 0x16 | 0x17
0x18 | 0x19 | 0x1A | 0x0B
 | … |  | 
Block 0
Block 1
Req (LBA: 0x01, Size: 2, DIR: W, Data: B, C)
Req (LBA: 0x07, Size: 1, DIR: W, Data: D)
Page Buffer
PPA

## Slide 19: Fine-Grained Mapping + Page Buffer
Write a page only when there are sufficient data blocks
Req (LBA: 0x04, Size: 1, DIR: W, Data: A)
LPA | PPA
0x00 | -
0x01 | -
… | -
0x04 | -
… | -
0x07 | -
… | …
0x00 | 0x01 | 0x02 | 0x03
0x04 | 0x05 | 0x06 | 0x07
0x08 | 0x09 | 0x0A | 0x0B
0x0C | 0x0D | 0x0E | 0x0F
0x10 | 0x11 | 0x12 | 0x13
0x14 | 0x15 | 0x16 | 0x17
0x18 | 0x19 | 0x1A | 0x0B
 | … |  | 
Block 0
Block 1
Req (LBA: 0x01, Size: 2, DIR: W, Data: B, C)
Req (LBA: 0x07, Size: 1, DIR: W, Data: D)
A |  |  | 
Page Buffer
PPA

## Slide 20: Fine-Grained Mapping + Page Buffer
Write a page only when there are sufficient data blocks
Req (LBA: 0x04, Size: 1, DIR: W, Data: A)
LPA | PPA
0x00 | -
0x01 | -
… | -
0x04 | 0x00
… | -
0x07 | -
… | …
0x00 | 0x01 | 0x02 | 0x03
0x04 | 0x05 | 0x06 | 0x07
0x08 | 0x09 | 0x0A | 0x0B
0x0C | 0x0D | 0x0E | 0x0F
0x10 | 0x11 | 0x12 | 0x13
0x14 | 0x15 | 0x16 | 0x17
0x18 | 0x19 | 0x1A | 0x0B
 | … |  | 
Block 0
Block 1
Req (LBA: 0x01, Size: 2, DIR: W, Data: B, C)
Req (LBA: 0x07, Size: 1, DIR: W, Data: D)
A |  |  | 
Page Buffer
PPA

## Slide 21: Fine-Grained Mapping + Page Buffer
Write a page only when there are sufficient data blocks
Req (LBA: 0x04, Size: 1, DIR: W, Data: A)
LPA | PPA
0x00 | -
0x01 | -
… | -
0x04 | 0x00
… | -
0x07 | -
… | …
0x00 | 0x01 | 0x02 | 0x03
0x04 | 0x05 | 0x06 | 0x07
0x08 | 0x09 | 0x0A | 0x0B
0x0C | 0x0D | 0x0E | 0x0F
0x10 | 0x11 | 0x12 | 0x13
0x14 | 0x15 | 0x16 | 0x17
0x18 | 0x19 | 0x1A | 0x0B
 | … |  | 
Block 0
Block 1
Req (LBA: 0x01, Size: 2, DIR: W, Data: B, C)
Req (LBA: 0x07, Size: 1, DIR: W, Data: D)
A |  |  | 
Page Buffer
PPA

## Slide 22: Fine-Grained Mapping + Page Buffer
Write a page only when there are sufficient data blocks
Req (LBA: 0x04, Size: 1, DIR: W, Data: A)
LPA | PPA
0x00 | -
0x01 | -
… | -
0x04 | 0x00
… | -
0x07 | -
… | …
0x00 | 0x01 | 0x02 | 0x03
0x04 | 0x05 | 0x06 | 0x07
0x08 | 0x09 | 0x0A | 0x0B
0x0C | 0x0D | 0x0E | 0x0F
0x10 | 0x11 | 0x12 | 0x13
0x14 | 0x15 | 0x16 | 0x17
0x18 | 0x19 | 0x1A | 0x0B
 | … |  | 
Block 0
Block 1
Req (LBA: 0x01, Size: 2, DIR: W, Data: B, C)
Req (LBA: 0x07, Size: 1, DIR: W, Data: D)
A | B | C | 
Page Buffer
PPA

## Slide 23: Fine-Grained Mapping + Page Buffer
Write a page only when there are sufficient data blocks
Req (LBA: 0x04, Size: 1, DIR: W, Data: A)
LPA | PPA
0x00 | -
0x01 | 0x01
… | -
0x04 | 0x00
… | -
0x07 | -
… | …
0x00 | 0x01 | 0x02 | 0x03
0x04 | 0x05 | 0x06 | 0x07
0x08 | 0x09 | 0x0A | 0x0B
0x0C | 0x0D | 0x0E | 0x0F
0x10 | 0x11 | 0x12 | 0x13
0x14 | 0x15 | 0x16 | 0x17
0x18 | 0x19 | 0x1A | 0x0B
 | … |  | 
Block 0
Block 1
Req (LBA: 0x01, Size: 2, DIR: W, Data: B, C)
Req (LBA: 0x07, Size: 1, DIR: W, Data: D)
A | B | C | 
Page Buffer
PPA

## Slide 24: Fine-Grained Mapping + Page Buffer
Write a page only when there are sufficient data blocks
Req (LBA: 0x04, Size: 1, DIR: W, Data: A)
LPA | PPA
0x00 | -
0x01 | 0x01
… | -
0x04 | 0x00
… | -
0x07 | -
… | …
0x00 | 0x01 | 0x02 | 0x03
0x04 | 0x05 | 0x06 | 0x07
0x08 | 0x09 | 0x0A | 0x0B
0x0C | 0x0D | 0x0E | 0x0F
0x10 | 0x11 | 0x12 | 0x13
0x14 | 0x15 | 0x16 | 0x17
0x18 | 0x19 | 0x1A | 0x0B
 | … |  | 
Block 0
Block 1
Req (LBA: 0x01, Size: 2, DIR: W, Data: B, C)
Req (LBA: 0x07, Size: 1, DIR: W, Data: D)
A | B | C | 
Page Buffer
PPA

## Slide 25: Fine-Grained Mapping + Page Buffer
Write a page only when there are sufficient data blocks
Req (LBA: 0x04, Size: 1, DIR: W, Data: A)
LPA | PPA
0x00 | -
0x01 | 0x01
… | -
0x04 | 0x00
… | -
0x07 | -
… | …
0x00 | 0x01 | 0x02 | 0x03
0x04 | 0x05 | 0x06 | 0x07
0x08 | 0x09 | 0x0A | 0x0B
0x0C | 0x0D | 0x0E | 0x0F
0x10 | 0x11 | 0x12 | 0x13
0x14 | 0x15 | 0x16 | 0x17
0x18 | 0x19 | 0x1A | 0x0B
 | … |  | 
Block 0
Block 1
Req (LBA: 0x01, Size: 2, DIR: W, Data: B, C)
Req (LBA: 0x07, Size: 1, DIR: W, Data: D)
A | B | C | D
Page Buffer
PPA

## Slide 26: Fine-Grained Mapping + Page Buffer
Write a page only when there are sufficient data blocks
Req (LBA: 0x04, Size: 1, DIR: W, Data: A)
LPA | PPA
0x00 | -
0x01 | 0x01
… | -
0x04 | 0x00
… | -
0x07 | 0x03
… | …
0x00 | 0x01 | 0x02 | 0x03
0x04 | 0x05 | 0x06 | 0x07
0x08 | 0x09 | 0x0A | 0x0B
0x0C | 0x0D | 0x0E | 0x0F
0x10 | 0x11 | 0x12 | 0x13
0x14 | 0x15 | 0x16 | 0x17
0x18 | 0x19 | 0x1A | 0x0B
 | … |  | 
Block 0
Block 1
Req (LBA: 0x01, Size: 2, DIR: W, Data: B, C)
Req (LBA: 0x07, Size: 1, DIR: W, Data: D)
A | B | C | D
Page Buffer
PPA

## Slide 27: Fine-Grained Mapping + Page Buffer
Write a page only when there are sufficient data blocks
Req (LBA: 0x04, Size: 1, DIR: W, Data: A)
LPA | PPA
0x00 | -
0x01 | 0x01
… | -
0x04 | 0x00
… | -
0x07 | 0x03
… | …
A | B | C | D
0x04 | 0x05 | 0x06 | 0x07
0x08 | 0x09 | 0x0A | 0x0B
0x0C | 0x0D | 0x0E | 0x0F
0x10 | 0x11 | 0x12 | 0x13
0x14 | 0x15 | 0x16 | 0x17
0x18 | 0x19 | 0x1A | 0x0B
 | … |  | 
Block 0
Block 1
Req (LBA: 0x01, Size: 2, DIR: W, Data: B, C)
Req (LBA: 0x07, Size: 1, DIR: W, Data: D)
A | B | C | D
Page Buffer
PPA
Flush (page write)
Fine-grained mapping significantly reduces the number of NAND flash operations:
3 writes (+1 read)  1 writes

## Slide 28: Drawbacks of Fine-Grained Mapping
Larger mapping table
  16-KiB mapping  4 bytes per 16-KiB page = 0.025%
  4-KiB mapping  4 bytes per 4-KiB page = 0.1%
  For a 2-TB SSD, 2-GB DRAM is required.
    Increases the SSD’s price and power/energy consumption
Data durability of written data
  Page buffers are implemented by using volatile memory (e.g., SRAM or DRAM).
  Once data is written to an SSD, the SSD needs to guarantee the data’s integrity even under sudden power off.
  Solution: power capacitors
Despites non-negligible drawbacks, fine-grained mapping is widely used in modern SSDs due to its high benefits

## Slide 29: Today’s Agenda
Fine-Grained Mapping
Multi-plane Operation-Aware Blk. Mgmt.

## Slide 30: Recap: Multi-Plane Operations
Concurrent operations on different planes
  Recall: Planes share WLs and row/column decoders
Opportunity: Planes can concurrently operate
Constraints: Only for the same operations on the same page offset
Plane0
Plane1
Plane2
Plane3
Page Buffers
Peripheral Circuits
Wordline Decoders
WL k
VREF
WL x
VPASS
(others)
Taget Page
Same voltage is
applied to all cells

## Slide 31: Multi-Plane-Aware Data Placement
To perform as many multi-plane operations as possible
  Flush Nplane pages at once after buffering them
Plane0
Plane1
Plane2
Plane3
Page Buffers
Peripheral Circuits
Page buffer
Wait for more writes
Full!

## Slide 32: Multi-Plane-Aware Data Placement
To perform as many multi-plane operations as possible
  Flush Nplane pages at once after buffering them
Plane0
Plane1
Plane2
Plane3
Page Buffers
Peripheral Circuits
Page buffer

## Slide 33: Multi-Plane-Aware Data Placement
To perform as many multi-plane operations as possible
  Flush Nplane pages at once after buffering them
  Need to keep the write points of all planes to be the same
    Superblock-based block management
Plane0
Plane1
Plane2
Plane3
Page Buffers
Peripheral Circuits
Page buffer

## Slide 34: Multi-Plane-Aware Block Management
Recap: For reducing the performance overhead of garbage collection, the FTL can select the block with the largest number of invalid pages (called a greedy policy).
Block0
Block1
BlockN-1
…
Plane
Block2
BlockN-2

## Slide 35: Multi-Plane-Aware Block Management
Recap: For reducing the performance overhead of garbage collection, the FTL can select the block with the largest number of invalid pages (called a greedy policy).
Block0
Block1
BlockN-1
…
Plane
Block2
BlockN-2
NINVALID = 3
NINVALID = 2
NINVALID = 5
NINVALID = 1
Full Blocks
Free
Valid
Invalid
Page Status
Victim Block
❶ Victim selection

## Slide 36: Multi-Plane-Aware Block Management
Recap: For reducing the performance overhead of garbage collection, the FTL can select the block with the largest number of invalid pages (called a greedy policy).
Block0
Block1
BlockN-1
…
Plane
Block2
BlockN-2
NINVALID = 3
NINVALID = 2
NINVALID = 5
NINVALID = 1
Full Blocks
Victim Block
❶ Victim selection
❷ Valid page copy
Free
Valid
Invalid
Page Status

## Slide 37: Multi-Plane-Aware Block Management
Recap: For reducing the performance overhead of garbage collection, the FTL can select the block with the largest number of invalid pages (called a greedy policy).
Block0
Block1
BlockN-1
…
Plane
Block2
BlockN-2
NINVALID = 3
NINVALID = 2
NINVALID = 5
NINVALID = 1
Full Blocks
Victim Block
❶ Victim selection
❷ Valid page copy
❸ Page invalidation
 Next Active Block
Free
Valid
Invalid
Page Status
Active Block (or Write Point)

## Slide 38: Multi-Plane-Aware Block Management
Recap: Planes in the same die can operate in parallel, but only when the page offsets are the same.
Block0
Block1
BlockN-1
…
Plane0
Block2
BlockN-2
…
Plane1
Peripheral (Decoder & Charge)
Die
3
2
5
1
0
7
3
2

## Slide 39: Multi-Plane-Aware Block Management
Recap: Planes in the same die can operate in parallel, but only when the page offsets are the same.
Block0
Block1
BlockN-1
…
Plane0
Block2
BlockN-2
…
Plane1
Peripheral (Decoder & Charge)
Die
3
2
1
0
3
2
5
7

## Slide 40: Multi-Plane-Aware Block Management
Recap: Planes in the same die can operate in parallel, but only when the page offsets are the same.
Block0
Block1
BlockN-1
…
Plane0
Block2
BlockN-2
…
Plane1
Peripheral (Decoder & Charge)
Die
3
2
1
0
3
2
5
7
Multi-plane write
Single-plane read
Single-plane read

## Slide 41: Multi-Plane-Aware Block Management
Recap: Planes in the same die can operate in parallel, but only when the page offsets are the same.
Block0
Block1
BlockN-1
…
Plane0
Block2
BlockN-2
…
Plane1
Peripheral (Decoder & Charge)
Die
3
2
1
0
3
2
5
7
2×Single-plane reads
2×Single-plane writes

## Slide 42: Multi-Plane-Aware Block Management
Recap: Planes in the same die can operate in parallel, but only when the page offsets are the same.
Block0
Block1
BlockN-1
…
Plane0
Block2
BlockN-2
…
Plane1
Peripheral (Decoder & Charge)
Die
3
2
1
0
3
2
5
7
4-page copy: can be done with 2×multi-plane reads & 2×multi-plane writes
 4×sigle-plane reads & 1×multi-plane write & 2×single-plane writes
Cannot perform multi- plane writes before using (or discarding) 2nd and 3rd pages of BlockN-1
in Plane1
Cannot perform multi- plane writes for future writes (due to different offsets)

## Slide 43: Multi-Plane-Aware Block Management
Superblock-based management: groups each block with the same index (i.e., vertical position) in different planes
Block0
Block1
BlockN-1
…
Plane0
Block2
BlockN-2
…
Plane1
Peripheral (Decoder & Charge)
Die
3
2
5
1
0
7
3
2

## Slide 44: Multi-Plane-Aware Block Management
Superblock-based management: groups each block with the same index (i.e., vertical position) in different planes
Block0
Block1
BlockN-1
…
Plane0
Block2
BlockN-2
…
Plane1
Peripheral (Decoder & Charge)
Die
3
2
5
1
0
7
3
2
❶ Valid page reads (5 SRs + 1 MR)

## Slide 45: Multi-Plane-Aware Block Management
Superblock-based management: groups each block with the same index (i.e., vertical position) in different planes
Block0
Block1
BlockN-1
…
Plane0
Block2
BlockN-2
…
Plane1
Peripheral (Decoder & Charge)
Die
3
2
5
1
0
7
3
2
❶ Valid page reads (5 SRs + 1 MR)
❷ Valid page writes (3 MRs)
Buffering

## Slide 46: Multi-Plane-Aware Block Management
Superblock-based management: groups each block with the same index (i.e., vertical position) in different planes
Block0
Block1
BlockN-1
…
Plane0
Block2
BlockN-2
…
Plane1
Peripheral (Decoder & Charge)
Die
3
2
5
1
0
7
3
2
❶ Valid page reads (5 SRs + 1 MR)
❷ Valid page writes (3 MRs)
Buffering
Pros: Keep performing multi-plane writes
Cons: More read/write operations  5 SRs + 1 MR + 3 MWs vs. 4 SRs + 1 MW + 2 SWs

## Slide 47: Multi-Plane-Aware Block Management
Offset management: Die level or SSD level?
Block0
Block1
BlockN-1
…
Plane0
Block2
BlockN-2
…
Plane1
Peripheral (Decoder & Charge)
…
Plane0
…
Plane1
Peripheral (Decoder & Charge)
Die0
Die1
…
Plane0
…
Plane1
Peripheral (Decoder & Charge)
Die2
…
Multi-plane operations can significantly improve SSD performance, but requires proper management in FTL

## Slide 48: P&S Modern SSDs Fine-Grained Mapping & Multi-Plane Operation-Aware Block Management
Dr. Mohammad Sadrosadati
Prof. Onur Mutlu
ETH Zürich
Fall 2022
14 December 2022